## Slide 1
FTA BEAM-TRACKING · CAMERA TIMING CHARACTERIZATION
Dual-Camera ROI Timing
Session Results — 2026-07-14
Two new sensor-level ROI modes, characterized end-to-end: frame content, throughput floors, closed-loop LED latency, and the live dual-camera demo app.
Raspberry Pi 5 + 2× OV9281 · target: 10 ms loop latency, 10–20 Hz disturbance band

## Slide 2
SESSION AGENDA
What we did today
• Added two new “quarter-tier” ROI modes to the patched driver — MODE_1280_200_ROI and MODE_640_100_ROI — pushing the vertical crop window from 400 real rows down to 200
• Validated frame content on both new modes, both cameras (headless capture, pixel stats, visual check)
• Ran throughput sweeps to find each new mode’s clean frame-duration floor — including one hang, recovered cleanly per the established procedure
• Ran closed-loop LED round-trip tests at each floor — the real control-relevant number, not just raw capture rate
• Found and fixed a latent bug in the ROI-move range, then extended the live dual-camera demo app to support the new, faster modes — validated live on the actual display
• Committed all of it (3 commits) and published a results-summary artifact
FTA Dual-Camera Timing — Session Results · 2026-07-14
2

## Slide 3
RECAP
Where this fits — the full mode progression
Mode | Rated ceiling | Achieved (dual) | Closed-loop | Mean latency
01 Stock 640×400 | 309.8 fps | 281.8 fps | 122 Hz | ~7 ms
02 1280×400 ROI | 296.5 fps | 283.6 fps (no win) | not run | —
03 640×200 ROI | 588.9 fps | ~527–530 fps | 206.6–207.9 Hz | 4.1–4.4 ms
04 1280×200 ROI — today | 542.6 fps | ~511–514 fps | 227.2–234.4 Hz | 3.3–3.4 ms
05 640×100 ROI — today | 1071.8 fps | 854–880 fps | 232.1–238.8 Hz | 3.5–3.7 ms
MODE_640_100_ROI is now the fastest and best closed-loop mode found in the project.
FTA Dual-Camera Timing — Session Results · 2026-07-14
3

## Slide 4
TODAY · 01
The two new “quarter-tier” modes
Same y_end = height + 15 windowing trick as the existing ROI modes, pushed one step further — 200 real sensor rows instead of 400. Both cloned register-for-register from their 400-row sibling, changing only y_end and y_output_size.
MODE_1280_200_ROI
unbinned · 200 real rows
• Rated ceiling: 542.59 fps
• No hang found down to 1600µs — throughput plateaus at ~511–514 fps instead
• Lowest mean closed-loop latency of any mode (3.3–3.4 ms), but the widest tail (up to ~30 ms)
MODE_640_100_ROI
binned · 200 real rows → 100 output
• Rated ceiling: 1071.81 fps — highest in the project
• Clean floor at 1050µs (~854–880 fps); hangs at 1000µs
• Best overall combination of closed-loop rate and latency tail-tightness of any mode tested
FTA Dual-Camera Timing — Session Results · 2026-07-14
4

## Slide 5
TODAY · 02
Frame content — validated clean
Headless capture (no live display needed): all 4 combinations negotiated the correct raw size, non-degenerate pixel stats, and visually coherent gradient/noise texture — no tearing, banding, or garbage.
1280×200 — cam 0
640×100 — cam 0
Mode / camera | Min | Max | Mean
1280×200 – cam0 | 2560 | 6912 | 4790.7
1280×200 – cam1 | 2816 | 11264 | 5084.9
640×100 – cam0 | 3328 | 7936 | 5412.5
640×100 – cam1 | 3840 | 16384 | 6111.1
16-bit raw values (R16 delivery quirk) — all four non-degenerate, no saturation/clipping pattern.
FTA Dual-Camera Timing — Session Results · 2026-07-14
5

## Slide 6
TODAY · 03
Throughput sweep — floors found for both
Mode | Rated | Clean floor | Achieved @ floor | Behavior at the edge
1280×200 ROI | 542.6 fps | 1600–1825µs | ~511–514 fps | Plateaus — no hang found in tested range
640×100 ROI | 1071.8 fps | 1050µs | 854–880 fps | Hangs at 1000µs (~5% below floor)
One hang hit, recovered cleanly
• 640×100 @ 1000µs timed out (20s) and was killed by the sweep orchestrator, orphaning two worker processes
• Checked state before acting: Sl / futex_do_wait (userspace lock wait, not kernel D-state) — confirmed safe to kill -9
• Verified via lsof that all /dev/video*/media* fds were released, then ran a known-good sanity check: 281.95/281.19 fps, matching baseline exactly — no reboot needed
FTA Dual-Camera Timing — Session Results · 2026-07-14
6

## Slide 7
TODAY · 04 — HEADLINE RESULT
Closed-loop LED round-trip test
 | 1280×200 @ 1775µs run 1 | run 2 | 640×100 @ 1050µs run 1 | run 2
Confirmed transitions (5s) | 1172 (0 timeouts) | 1136 (0 timeouts) | 1194 (0 timeouts) | 1160 (0 timeouts)
Achieved capture fps | 496.3 / 495.7 | 491.8 / 492.6 | 860.6 / 860.8 | 858.3 / 861.9
Mean latency (cam0/cam1) | 3.38 / 3.30 ms | 3.39 / 3.29 ms | 3.50 / 3.54 ms | 3.72 / 3.65 ms
Max latency (cam0/cam1) | 29.57 / 9.18 ms | 27.33 / 13.58 ms | 12.70 / 7.71 ms | 15.59 / 21.90 ms
Effective closed-loop freq | 234.4 Hz | 227.2 Hz | 238.8 Hz | 232.1 Hz
MODE_640_100_ROI: 0 timeouts across 2 runs, mean latency comfortably under Phil’s 10 ms target, and the best effective closed-loop rate found in the project.
FTA Dual-Camera Timing — Session Results · 2026-07-14
7

## Slide 8
ACROSS THE PROJECT
Effective closed-loop toggle rate, by mode
Chart: 
| 640×400 stock | 640×200 ROI | 1280×200 ROI — today | 640×100 ROI — today
Closed-loop Hz (best of runs) | 122 | 207.9 | 234.4 | 238.8
1280×400 ROI omitted — no throughput win over stock, so closed-loop was never characterized for it.
FTA Dual-Camera Timing — Session Results · 2026-07-14
8

## Slide 9
ACROSS THE PROJECT
Mean per-camera latency vs. the 10 ms target
Chart: 
| 640×400 stock | 640×200 ROI | 1280×200 ROI — today | 640×100 ROI — today
Mean latency (ms) | 7 | 4.35 | 3.34 | 3.6
Every ROI mode clears Phil’s 10 ms mean-latency target (chart scale fixed at 0–12 ms for comparison).
FTA Dual-Camera Timing — Session Results · 2026-07-14
9

## Slide 10
TODAY · 05
Live demo app — validated on the fastest mode
• Found a latent bug: the ROI-move range was hardcoded to the original modes’ 400-row window (max y_start=400) — would’ve silently misbehaved on the new 200-row modes (real range is 0–600)
• Fixed by querying the driver’s live crop height on every call instead of assuming it; regression-checked against the original 640×200 mode first
• Extended roi_live_demo.py so ‘b’ toggles binned↔unbinned within whichever “tier” a camera is in — the app now reaches all four ROI modes, including the fastest
Live on the actual display, 640×100 mode:
FTA Dual-Camera Timing — Session Results · 2026-07-14
10

## Slide 11
STATUS
Open question for Phil, and what's next
BLOCKS FURTHER OPTIMIZATION
Does the real FTA control algorithm need discrete step-and-confirm (~120–240 Hz, mode-dependent) or continuous latest-frame tracking (~280–880 fps, no confirmation step)? These are genuinely different ceilings — which one is relevant determines where further tuning is worth spending.
Not yet done
• Mid-stream set_selection write validation (background-capture + external-write correlation check) hasn’t been repeated on the two new modes specifically
• Hardware and driver remain stable: tainted stayed at 4096 (no D/W) through every test today, i2c@80000 continues to enumerate cleanly
• All work committed today: 3 commits (new modes + validation, closed-loop results, live-demo fix)
FTA Dual-Camera Timing — Session Results · 2026-07-14
11