## Slide 1
FTA BEAM-TRACKING · CLOSED-LOOP CONTROL
FTA Position Calibration & Control Law
Session Results — 2026-07-23
Found the real FTA-driving firmware, measured real serial latency and safe throughput,
designed the PI control law, and characterized actual step response on both axes.
Raspberry Pi 5 + OV9281 · NUCLEO-L432KC "FTA Controller" · target: 10 ms loop latency, 10–20 Hz disturbance rejection

## Slide 2
SESSION AGENDA
What we did today
• Started from the idea: sweep the FTA over a grid, fit a matrix from actuator command to camera centroid, invert it to command a position
• Went down a wrong-repo path first (ucsbdeepspace/fta_calibration, an old pyboard rig) — corrected once the real firmware was found
• Found the actual “FTA Controller” Nucleo firmware (ucsbdeepspace/7-element-array, lock_in_2): serial, not I2C — already has grid_scan, PID, DAC drive
• Built fta_calibration.py (grid_scan reuse) and estimated, then measured, the real serial-vs-I2C performance gap
• Designed the PI control law; built fta_step_response_test.py to get the actuator dynamics data gain tuning actually needs
• Found the amp was unplugged, fixed it, and characterized real step response — both axes, converted px → microns
FTA Position Calibration · Session Results · 2026-07-23
2

## Slide 3
TODAY · 01
The idea: calibrate, then close the loop
Sweep the FTA over a grid of actuator setpoints, record where each one puts the beam centroid, fit a matrix, invert it.
3×3 homogeneous affine
DAC setpoint → centroid pixel
• 2×2 gain block + offset, fit via least squares
• Fits DAC→pixel: DAC is commanded exactly, centroid is the noisy side
• Inverting it gives centroid→DAC to command a target position
PI control law (designed)
feedforward + continuous trim
• One-time feedforward via the fitted M_inv, then continuous per-frame PI — a regulator problem, not tracking
• Pixel error decoupled into DAC-space via the calibration's own gain-block inverse first
• Anti-windup, measured dt, freeze-on-lost-beam — all required, not optional
FTA Position Calibration · Session Results · 2026-07-23
3

## Slide 4
TODAY · 02
A wrong assumption, corrected
Started extending the existing I2C link for actuator commands, before finding the actual FTA-driving Nucleo firmware.
Assumed
new I2C actuator packet
• Extend nucleo_i2c_sender.py with a second packet type for DAC setpoints
• Based on the wrong reference repo (fta_calibration, an old pyboard rig)
• Fully reverted once the real repo was found — nucleo_i2c_sender.py unchanged
Actual: 7-element-array
USB-serial, 460800 baud
• “FTA Controller” STM32L432 firmware already exists — matches this project's NUCLEO-L432KC
• set_x / set_y, a full PID framework, and a working grid_scan that microsteps a grid, streams position + ADC per point
• grid_scan's smooth travel reused as-is for fta_calibration.py — no firmware changes needed
FTA Position Calibration · Session Results · 2026-07-23
4

## Slide 5
TODAY · 03
fta_calibration.py: reuses grid_scan
• Sends grid_scan x1 y1 x2 y2 as-is; listens for the firmware's “SD <adc> <x> <y>” lines purely as a per-point capture trigger
• On each trigger, captures and averages --frames-per-point camera centroids via find_beam_blob (duplicated per this project's convention, not imported)
• Fits the 3×3 affine via least squares, inverts it, warns on a near-singular gain block or large RMS residual
• Saves the raw sweep + both matrices to results/fta_calibration_<timestamp>.npz
• Sends the firmware's ISR-level “!” emergency-stop byte on Ctrl-C so an interrupted run doesn't leave the FTA mid-scan
• Fit math validated against synthetic data (recovers a known matrix, inverse round-trips exactly) — not yet run as a real sweep
FTA Position Calibration · Session Results · 2026-07-23
5

## Slide 6
TODAY · 04 — HEADLINE RESULT
Real serial latency, safe ceiling found
Fire-and-forget rate-sweep: safe up to ~1600Hz, then a sharp cliff.
Mode | Command | Mean | p99 | Max
ping | get_status (read-only) | 2.14 ms | 3.00 ms | 5.53 ms
setpos | set_x (wait-for-ack) | 1.26 ms | 2.03 ms | 2.14 ms
Dropped commands, out of 300 sent per rate (Hz)
Chart: 
| 100 | 800 | 1400 | 1600 | 1800 | 2000 | 2500
Dropped commands (of 300) | 0 | 0 | 0 | 0 | 36 | 72 | 116
FTA Position Calibration · Session Results · 2026-07-23
6

## Slide 7
TODAY · 05
PI control law, worked through in detail
• e_pixel = target − measured; e_dac = A_inv · e_pixel (decouples via the calibration's own gain block)
• integral += e_dac · dt (measured dt, not assumed-constant) → u = current_dac + Kp·e_dac + Ki·integral
• Anti-windup: stop accumulating the integral once u would saturate the DAC clamp
• Start with PI, not PID — a derivative term would amplify the centroid's own detection noise
• Rough bandwidth sanity check: total loop delay (~5–6ms) implies a usable ceiling around ~29Hz — rejecting 10–20Hz is plausible but not with huge margin
• Gains can't be derived from the calibration matrix alone — it's a static map; dynamic (speed/overshoot) data has to come from a real step-response test
FTA Position Calibration · Session Results · 2026-07-23
7

## Slide 8
TODAY · 06 — HEADLINE RESULT
Hardware gap found and fixed
The voice-coil amplifier was unplugged — sweeping the full DAC range moved nothing until it was reconnected.
Diagnosed methodically
not assumed
• Confirmed a real beam was visible and stably detected first
• Swept the full DAC range on both axes — zero movement
• Checked amp_enable/drv_enable explicitly before concluding it was a deeper wiring gap
• User found it: the amplifier was simply unplugged
Real finding: ~90° axis rotation
confirmed on both axes
• DAC-x mostly drives pixel-y, DAC-y mostly drives pixel-x — a real mounting fact, not a bug
• Exactly why the control law decouples via the full 2×2 matrix inverse instead of assuming x↔x, y↔y
• Also caught and fixed a real bug in the test script itself: it was analyzing the wrong (weak) pixel axis by default
FTA Position Calibration · Session Results · 2026-07-23
8

## Slide 9
TODAY · 07 — HEADLINE RESULT
Small steps settle far faster than big ones
Axis | Step | Δ (µm) | Settling | Overshoot
x | 95→2000 (large) | 483µm | 793 ms | 22.4%
x | 2000→2100 (small) | 28µm | 45 ms | 42.3%
y | 95→2000 (large) | −364µm | 1183 ms | 0.0%
y | 2000→2100 (small) | −20µm | 83 ms | 0.0%
Settling time by step size (ms)
Chart: 
| x: large step | x: small step | y: large step | y: small step
Settling time (ms) | 793 | 63 | 1183 | 83
FTA Position Calibration · Session Results · 2026-07-23
9

## Slide 10
STATUS
Open questions and what's next
BLOCKS GAIN TUNING
Rise time is still unmeasured — detection drops out during the fastest part of a transition (motion blur); needs a faster camera mode or a different sensor approach.
• Per-axis gains may be needed — y's small-step settling spread (22–144ms) is wider than x's tighter 45–80ms cluster
• Board consolidation question still open: I2C centroid-receiving and serial FTA-driving are two separate, incompatible firmware images on the same physical Nucleo
• Real fta_calibration.py sweep against real hardware — not yet run for real, only validated against synthetic data
• PI control law itself — designed, not yet implemented as a script; needs the rise-time gap closed first for confident gain selection
FTA Position Calibration · Session Results · 2026-07-23
10